## Slide 1: Sulfur Based Thermochemical cycles for Hydrogen Production
Peter Ota

## Slide 2: Content Overview
Thermochemical Cycles
Heat sources for thermochemical cycles
Iodine-Sulfur cycle
Bromine-Sulfur hybrid cycle
Hybrid sulfur cycle
Conclusion

## Slide 3: Thermochemical Cycles
Combine heats source with chemical reactions to split water into hydrogen and oxygen
The chemical compounds used to separate hydrogen and oxygen are recycled
Temperatures between 750°C and 1000°C are optimal for thermochemical cycles
Can reach an efficiency of 50% (electrolysis hydrogen production efficiency ≈ 20-40%)
Sulfur based cycles are the most promising with current technology

## Slide 4: Heat sources
Nuclear Heat
  Current commercial reactors have a maximum temperature of ~700°C which is less than required for Thermochemical cycles
  New high temperature reactors would be required
Concentrated Solar Power
  Only other carbon neutral source that can reach temperatures above 800°C
  No current solar plants used to create hydrogen using thermochemical cycles

## Slide 5: Iodine-Sulfur cycle
Rejected Heat
Hydrogen
Oxygen
900°C
400°C
Heat
H2O
Sulfur
Circulation
Iodine
Circulation
SO2 + H2O
I2
2HI + H2SO4
I2 + H2O + SO2
H2SO4
SO2 + H2O
2HI
H2
½O2
I2
Efficiency of 30-50%
Heat is used to separate hydrogen from iodine & Oxygen from Sulfuric acid

## Slide 6: Bromine-Sulfur Hybrid cycle
Rejected Heat
Hydrogen
Oxygen
900°C
Heat
H2O
Sulfur
Circulation
Bromine
Circulation
SO2 + H2O
Br2
2HBr + H2SO4
Br2 + H2O + SO2
H2SO4
SO2 + H2O
2HBr
H2
½O2
Br2
Efficiency of 40%
electrolysis is used to remove hydrogen from bromine
The sulfur loop is identical to the sulfur-Iodine cycle
Electricity

## Slide 7: Hybrid Sulfur Cycle
H2 + H2SO4
2H2O + SO2
H2O
Hydrogen
Oxygen
Electrolysis
Sulfur
Circulation
H2SO4
H2O + SO2 + ½O2
Heat (>800°C)
H2SO4
H2O + SO2
Electricity
Efficiency of 40-50%
Developed by Westinghouse in 1976
Uses electrolysis and thermochemical reactions
Outperforms the Sulfur-Bromine hybrid cycle without using a Halogen

## Slide 8: Status of thermochemical cycles
Westinghouse stopped research of the Hybrid-Sulfur cycle when oil prices dropped in 1986
General Atomics, Sandia national labs and University of Kentucky lead research in the united states

## Slide 9: Conclusion
Sulfur-Iodine cycle is the most efficient Halogen cycle
Sulfur-Hybrid cycle is the most efficient hybrid cycle
All of the sulfur thermochemical cycles are more efficient than just electrolysis
A new reactor or solar thermal plant would be required for commercial hydrogen creation

## Slide 10: References
Ragheb, M. “Thermochemical Iodine Sulfur for Hydrogen Production,” Sept. 26, 2014.
Perret, R. “Solar Thermochemical Hydrogen Production Research,” may, 2011
“Nuclear Hydrogen R&D Plan,” Mar. 2004, Department Of Energy, http://www.hydrogen.energy.gov/pdfs/nuclear_energy_h2_plan.pdf
http://www.ika.rwth-aachen.de/r2h/index.php/HT_Reactor_Associated_to_Thermo-chemical_Cycles