## Slide 1: Feasibility of 100% Zero Emission Vehicles by 2035 in Illinois Powered by Renewable Energy Sources Only
Sonia Chandra
UIUC M.Eng in Energy Systems
schand58@illinois.edu
NPRE 498

## Slide 2: Background
5th largest energy-consuming state in the nation
6th largest petroleum-consuming state in the nation
1,014 trillion BTU annually
$21,260 million annually

## Slide 3: Background
Destination: Zero Carbon
Make all new cars electric by 2035.
Make all buses electric by 2030.
Double the number of people who travel on foot, bike or public transit by 2030.

## Slide 4: Types of Electric Vehicles’s (EVs)
Plug-in hybrid
Battery electric
Hydrogen fuel cell

## Slide 5: Zero Emission Vehicle (ZEV) program
Managed by California Air Resources Board (CARB)
Adopted by 10 states: Colorado, Connecticut, Maine, Maryland, Massachusetts, New Jersey, New York, Oregon, Rhode Island, and Vermont
Each automaker is assigned ZEV credits
Tesla Model S : 3.3 credits
Nissan Leaf: 1.8 credits
PHEVs  43% of credits
BEVs & FCEVs 57% of credits

## Slide 6: Constraints
Total Energy Demand: 100% EV’s
Renewable Energy Sources: Nuclear, Wind and Solar
Business As Usual (BAU) Projections
Feasibility:
Growth in Renewable Energy > Total Energy Demand
Current grid system can supply and transmit total energy demand
Savings from petroleum > Cost of infrastructure (4 charging ports to80% current gas stations)

## Slide 7: Energy Demand from 100% EV’s
Total Miles Driven in IL / Year
Average car (ICE) fuel consumption= 25mpg
Illinois motor gasoline consumption (2019) = 105,720,000 Barrels
Total miles travelled in IL/ year (2019) =1.1 x10^11 miles (110 Billion Miles)
Average miles per driver = 12,581 miles
Current % of EV’s in IL = 0.3 % (12400)
Total Energy Demand
Average EV energy consumption=314Wh/mile
Total Energy Demand (100%)= 1.1 x 10^11 miles x 314Wh/mile
35 TWh

## Slide 8: Energy Savings from 100% EV’s
Current Energy Demand (gasoline) = 180 TWh
145 TWh savings
Energy Savings 180TWh  35TWh = 80%

## Slide 9: Feasibility on IL Grid System
Current net electricity generation = 184TWh
Total Retail Sales = 138TWh
Energy not consumed = 46TWh (25%)
Additional energy needed = 35 TWh

## Slide 10: Anticipated Renewable Energy Generation in 2035
Source (Thousand MWh) | Nuclear | Wind | Solar | Total
Current Generation (2020) | 100246 | 17111 | 92.85 | 
Expected Generation (2035) | 105356 | 86486 | 185.5 | 
Additional Energy | 5110 | 69375 | 92.65 | 74577.65
74 TWh
47%  Powering EV’s

## Slide 11: Nuclear Power in Illinois
Without nuclear energy: 69TWh
51%  Powering EV’s

## Slide 12: Solar Energy in IL
SEIA: Path to 100
RPS: 25% by 2025 to 40% by 2030
REC procurement from 10 million by 2020 to 45 million by 2030
50/50 split from solar and wind.

## Slide 13: Residential PV
Expected to grow 1700% in next decade
Residential PV 1400 MWh  2TWh

## Slide 14: Cost of Infrastructure
AC Level 2 Vehicle Range Added per Charging Time and Power
10 mi/hour @ 3.4kW
20 mi/hour @ 6.6kW
60 mi/hour @ 19.2 kW
208/240VAC/20-100A (16-80A continuous)
EVSE | Cost
Installation | $4200
Pedestal Equipment | $4500
Operation & Maintenance | $686
Total | $9386

## Slide 15: Cost of Infrastructure
Number of charging ports =12,212
Total Cost = $114.6 Million
Cost of petroleum/year =$4.6 Billion

## Slide 16: Benefits of EV Market Expansion on Energy Storage Systems
Allows EV’s to be used in lieu or in conjunction with electricity storage in emergencies/supply shortages
As EV increases amount of energy purchased at night, it reduces energy-time shift and time-off use energy cost management
Leads to economies of scale and lower prices for advanced battery systems
Increases grid integration and system management

## Slide 17: Current EV Incentives
EV exemption from state emissions testing
ComEd offers 3 EV rate plans for residential customers
Illinois Electric Co-op members may be eligible to finance their EV at 0.5% interest
City of Naperville offers $30 per kW up to $3,000 (filed on behalf of customer)

## Slide 18: EU Electric Vehicle Targets
30 million electric cars by 2030
Currently: 1.8 million electric and plug-in hybrid vehicles registered in Europe
High-speed rail traffic to double by 2030
Scheduled travel between cities of under 300 kilometers (186 miles) to become carbon-neutral
Zero-emission large aircraft and vessels should be “ready for market” by 2035

## Slide 19: Questions?
Thank You

## Slide 20: References
https://ev-database.org/cheatsheet/energy-consumption-electric-car
https://www.iea.org/reports/fuel-consumption-of-cars-and-vans
https://www.epa.gov/automotive-trends/highlights-automotive-trends-report
https://afdc.energy.gov/data/10962
https://www.thezebra.com/resources/driving/average-miles-driven-per-year/#average-miles-driven-per-year-by-state
https://www.valuepenguin.com/auto-insurance/car-ownership-statistics
https://www.solarpowerworldonline.com/2019/06/illinois-agency-says-state-wont-reach-rps-of-25-by-2025-unless-legislation-changes/
https://ilenviro.org/energy/renewable-energy/
https://afdc.energy.gov/files/u/publication/evse_cost_report_2015.pdf