## Slide 1
Application of Redox-active Polymers (RAPs) for energy Storage in Redox-Flow Batteries
Zirui Wang
December 4th, 2023
NPRE 498, Final Presentation

## Slide 2: Short Personal Bio
2nd year graduate student in Materials Science and Engineering
  BS 2018, Materials Science and Engineering, University of Illinois, Urbana-Champaign
Currently working with in the research group of Prof. Joaquín Rodríguez-López
  Energy storage in batteries, fuel cells, etc.
  High-throughput/Automated electrochemical methods
  Electrochemical CO2 capture
  Molecular electrocatalysis
  Electrochemical cancer detection/treatment
  Check out our group website for more works! (http://faculty.scs.illinois.edu/rodriguez-lopez/research.html)
1

## Slide 3: Outline
Outline Introduction Results and Discussion Summary
Introduction:
  Why batteries are important
  Theory, setup, and benefits of redox-flow batteries (RFBs)
  Traditional RFBs
  Problems with traditional RFBs
Results and discussion
  Redox-active polymers (RAPs): introduction
  The use of conductive polymers in RFBs
  The use of polymers with redox-active pendants in RFBs
Summary:
  Current state-of-art
  Future directions
2

## Slide 4: Global Warming, As We All Know
Global warming forces human to find alternatives to fossil fuels
Cleaner energy conversion methods as well as energy storage becomes overly important
  Wind power
  Solar power
  Batteries and fuel cells
Outline Introduction Results and Discussion Summary
https://theglobalobservatory.org/2021/12/new-climate-data-visualizations-2021/
3

## Slide 5: Why Batteries?
Replenishable
  Typically, only electricity is required to recharge a battery
Versatile
  Can be used in lots of platforms ranging from portable electronic devices to spacecrafts
Fast energy conversion
Negligible intermittence
Good energy density and specific power
Minimal carbon emission
Outline Introduction Results and Discussion Summary
4

## Slide 6: Electrochemical Energy Storage
The energy cost of chemical reactions is described by the Gibbs free energy ()
The accessible electrical energy from a heterogenous electron transfer reaction () is described by the following equation:
: Free energy difference between B and A
n: number of electrons transferred
F: Faraday’s constant (96485 C/mol)
Electricity can be obtained from spontaneous chemical reactions ()
Outline Introduction Results and Discussion Summary
Example: Lithium-ion battery
  Cathode:
  Anode:
  Overall:
  Typical cell voltage: 3.7 V
Journal of the American Chemical Society 2013, 135 (4), 1167–1176
5

## Slide 7: Redox-flow Batteries (RFBs)
RFBs have two tanks of electrolyte
Electrolytes are pumped into the electrochemical cell in the middle
Electricity is obtained via spontaneous reactions
Simply refilling the electrolyte tanks to recharge the RFB
  No limit on capacity
Traditional RFB:
  Vanadium-based
  Anode:
  Cathode:
  Total:
Problems:
  Low energy density due to the presence of tanks
  Low cell voltage
  Not cost effective due to vanadium price
Outline Introduction Results and Discussion Summary
Molecules 2015, 20, 11, 20499-20517
Catholyte
Anolyte
Can these problems be solved?
6

## Slide 8: Redox-active Polymers (RAPs) As New Electrolytes for Redox-flow Batteries
A polymer is a large molecule (macromolecule) that consists of a large number of repeating units.
Redox-active polymers (RAPs) can transfer electrons, which means they can be oxidized (lose electrons) or reduced (accept electrons)
Two types of RAPs:
  Redox-active group embedded polymers
  Redox-active pendant-bearing polymers
Outline Introduction Results and Discussion Summary
https://en.wikipedia.org/wiki/Polypyrrole
Joule 2017, 1 (4), 739–768
7

## Slide 9: Redox-Active Group Embedded Polymers and Redox Targeting
The repeating units of redox-active group embedded polymers can be oxidized or reduced.
Once a single unit is oxidized/reduced, the charge (electron/hole) will propagate throughout the polymer chain, so redox-active group embedded polymers are conductive.
Conductive polymer can mediate the charges between the reduced (Red) and the oxidized (Ox) form of the electrolyte via chemical reactions.
Example:
The oxidized form of the catholyte gets reduced and is pumped into the tank that contains conductive polymer -> Conductive polymer reacts with the reduced form of the catholyte, taking away the charge to power the load as well as regenerating the original form of the catholyte
Outline Introduction Results and Discussion Summary
Redox-active repeating units
Charged state
Ox
Ox
Ox
Ox
Chemical reaction
Discharged state
Red
Red
Red
Red
Catholyte
Conductive polymer
Anolyte
ACS Applied Materials & Interfaces 2022, 14 (5), 6638–6648
8

## Slide 10: Redox Targeting: The Significance
Instead of storing charges inside the liquid form electrolytes, redox targeting provides a way to store charges in solid-state media, resulting in a much higher energy density.
Because fresh electrolyte is conservative and can be regenerated throughput the process, replacing the electrolyte frequently is unnecessary.
The only component that needs to be replaced is the redox-active polymers.
However, this technique is mostly still in the research stage.
Outline Introduction Results and Discussion Summary
9

## Slide 11: Redox-Active Pendant Bearing Polymers
The backbone of the polymer is not conductive.
However, there are lots of redox-active functional groups that can be attached (grafted) to the backbone.
Each pendant group can be individually oxidized or reduced.
Synthesis pathways for these polymers are mostly well-defined.
The behavior of redox-active pendant bearing polymers is highly dependent on:
  Solution environment
  Molecular structure
  Molecular weight
Outline Introduction Results and Discussion Summary
Non-conductive backbone
Redox-active pendants
Accounts of Chemical Research 2016, 49 (11), 2649–2657
10

## Slide 12: Redox-Active Pendant Bearing Polymers: The Significance
The possibility of accepting/donating multiple electrons within a single polymer molecule gives rise to an enhanced energy density.
Theoretically, the capacity of the battery is only limited by (1) the allowable number of redox-active pendants on the polymer backbone (2) the solubility limit of the redox-active polymer
Fairly straightforward and cheap synthesis
However, the behavior of different redox-active pendant bearing polymers is very complicated inside different solutions. A more systematic understanding is still required for commercialization.
Outline Introduction Results and Discussion Summary
11

## Slide 13: Summary
Traditional inorganic electrolyte-based redox-flow batteries have energy density and cost problems.
Redox-active polymers are attractive solutions to the forementioned problems.
Redox-active group embedded polymers (conductive polymers) allows a much higher energy density, as it allows charges to be stored in a solid-state medium instead of liquid-state.
Redox-active pendant bearing polymers also allows a higher energy density due to the presence of multiple redox-active groups in one polymer molecule and is closer to be commercialized.
In general, more research is required in the field of redox-active polymers.
Thanks! Any Questions?
Outline Introduction Results and Discussion Summary
12