## Slide 1: COMPRESSEDAIR ENERGY STORAGE
Sarah Long
NPRE 498
May 3rd, 2021

## Slide 2: Background Information What is CAES ?
A means of storing energy for later use in the form of compressed air
Energy is stored in an underground reservoir
The air can be released to a combustor in a gas turbine to generate electricity when needed

## Slide 3: How it works
Consists of an underground air storage, air compressor, motor, and a turbine

## Slide 4: Why is CAES important
Reduces CO2 emission
Increases energy savings
Improved system stability
Less maintenance cost
Longer lifetime

## Slide 5: Challenges
Location
Loss of energy
Outside fuel source needed for diabatic systems

## Slide 6: Diabatic
Energy storage system based on the compression of air and storage in geological voids
Similar to a gas turbine
When energy is needed the release of air is heated via combustion using natural gas or fuel

## Slide 7: Adiabatic
When the air is compressed, heat is not released into the surrounding
Instead captured in a heat storage facility
Used to achieve significant reduction in fuel consumption

## Slide 8: The First CAES
Developed by E.ON-Kraftwerk in Huntorf, Germany in 1978
Two salt caverns located
600 meters below ground
Has storage capacity of
300,000 m3
Daily charging cycle of 8 hours with 2 hours of expansion producing 290 MW of rated power

## Slide 9: Alabama Electric Corporation
Located in McIntosh, Alabama
Built in 1991
Produces 110 MW
Storage capacity of 560,000 m3
One salt caverns at a depth of 450m
Has slightly better cycle efficiency than Germany plant

## Slide 10: New developments
Alternatives are also being considered
Project in Norton, Ohio
European facility called RICAS 2020 project
UK CRYOBattery

## Slide 11: New developments
Hydroster plant in Ontario, Canada
First commercial plant
2019
Provides 7 MWh of capacity

## Slide 12: New developments
Hydroster plant in Rosamond California

## Slide 13: In Conclusion
CAES is a good choice for storing energy
Better for the environment
More reliable energy source
Using new adiabatic designs CAES will not consume any more fuel
Only two current plants operating
Future plants are on the way

## Slide 14: Refrences
https://www.hydrostor.ca/goderich-a-caes-facility/
https://www.energy-storage.news/news/construction-of-250mwh-liquid-air-cryobattery-has-begun-in-uk
https://www.cleveland.com/business/2013/07/firstenergy_postpones_project.html
http://www.fze.uni-saarland.de/AKE_Archiv/AKE2003H/AKE2003H_Vortraege/AKE2003H03c_Crotogino_ea_HuntorfCAES_CompressedAirEnergyStorage.pdf
https://interestingengineering.com/compressed-air-energy-storage-caes-systems