## Slide 1: Terse Critique of article “Pee Power”
Presentation by Bert Stunkard
NPRE 498 ES
October 13, 2010

## Slide 2: Source article
Hazel Muir, “Pee Power”, in New Scientist, Vol. 207(2774), August 21, 2010, p37-39.
Hazel Muir is a free-lance science writer based in the United Kingdom.
Has written several feature articles for New Scientist

## Slide 3: Urea instead of water for H2
Hydrogen atoms less tightly bound. 0.37 [v] to free H2, versus 1.23 [v] for H2O
Nickel electrodes instead of precious metals
Solution or solid. Less troublesome storage and transport than H2.
Fuel cell can produce electricity directly from Urea.
Some estimate $1/kg H2 from urea

## Slide 4: Adblue
Fueling stations in Europe and Asia often sell 32.5% urea solution for (mandated) nitrogen oxide scrubbing
Launching point for urea fuel cells

## Slide 5: Problems with “Pee”
Urea only 2% of human urine
Further diluted in sewage systems
Urea becomes ammonia, due to both chemical and bacteria action.
Sewage, animal waste useful, under-utilized fertilizer. (Consider biochemical fuel-cells)
Urea current produces CO2 and manufactured from natural gas.
Niche player